## Slide 1
Azure Virtual Network Routing Appliance
Lab 240 - Scalable east-west routing in a hub-and-spoke topology using Terraform (azurerm + azapi)
Azure Network Course
github.com/HoussemDellai/azure-network-course

## Slide 2
Agenda
Azure Network Course | Lab 240 - Virtual Network Routing Appliance
2
▪ What is a Virtual Network Routing Appliance?
▪ Routing appliance vs. NVA / firewall
▪ Lab architecture and address plan
▪ Terraform implementation: hub, appliance, spokes, peering
▪ User Defined Routes steering traffic to the appliance
▪ Traffic flow, deployment and verification
▪ Troubleshooting and key takeaways

## Slide 3
What is a Virtual Network Routing Appliance?
Azure Network Course | Lab 240 - Virtual Network Routing Appliance
3
▪ Managed routing service deployed into a dedicated subnet of a VNet (resource type Microsoft.Network/virtualNetworkAppliances).
▪ Advanced routing beyond default Azure routing for traffic between subnets and VNets.
▪ East-west focus manages traffic between subnets; it is not a security enforcement point like a firewall.
▪ Scale-out and performance multiple instances for higher aggregate throughput (up to Tbps) and better NVA workload performance.
▪ Used together with UDRs, NSGs, admin rules, VPN / ExpressRoute gateway and NAT Gateway.
Reference architecture (Microsoft)

## Slide 4
Routing appliance vs. NVA / Firewall
Azure Network Course | Lab 240 - Virtual Network Routing Appliance
4
Aspect | Virtual Network Routing Appliance | NVA / Azure Firewall
Primary purpose | Routing and traffic management | Security inspection and filtering
Traffic scope | East-west between subnets / VNets | East-west, north-south, internet egress
Security enforcement | None - use NSGs / admin rules | Yes - FW rules, IDPS, TLS inspection
Scaling | Scale-out, bandwidth set per appliance (10 Gbps in lab) | Depends on SKU / VM size
Next hop type in UDR | VirtualAppliance -> appliance private IP | VirtualAppliance -> NVA / FW private IP

## Slide 5
Lab architecture: hub and spokes
Azure Network Course | Lab 240 - Virtual Network Routing Appliance
5
vnet-hub 172.16.0.0/12
VirtualNetworkApplianceSubnet
hub-routing-appliance
172.16.0.0/24 - 10 Gbps
AzureBastionSubnet
Azure Bastion - 172.16.1.0/27
vnet-spoke1 10.1.0.0/16
snet-spoke1-workload 10.1.0.0/24
vm-linux-spoke1
vnet-spoke2 10.2.0.0/16
snet_spoke2_workload 10.2.0.0/24
vm-linux-spoke2
Peering
Peering
Design points
▪ Hub uses a large 172.16.0.0/12 space
▪ Spokes use 10.x.0.0/16
▪ Spoke-to-spoke traffic has no direct peering
▪ UDRs force it through the appliance
▪ Bastion gives private SSH access
Spoke VMs: Ubuntu 24.04 Spot VMs (Standard_D2ads_v7), no public IP. Resource groups: rg-hub-240, rg-spoke1-240, rg-spoke2-240.

## Slide 6
Terraform implementation overview
Lab folder: 240_vnet_routing_appliance
Azure Network Course | Lab 240 - Virtual Network Routing Appliance
6
File | Purpose
providers.tf / variables.tf | azurerm >= 4.37, azapi >= 2.12, Terraform >= 1.11; prefix "240"
hub_rg.tf, hub_vnet.tf | Hub resource group, VNet 172.16.0.0/12, appliance and Bastion subnets
hub_routing_appliance.tf | Routing appliance resource (azapi) + private IP output
bastion.tf | Azure Bastion with public IP for SSH access to spoke VMs
spoke1_*.tf / spoke2_*.tf | Resource group, VNet, workload subnet, VM, peering, route table

## Slide 7
Deploying the routing appliance
No azurerm resource yet - the lab uses the azapi provider
Azure Network Course | Lab 240 - Virtual Network Routing Appliance
7
resource "azapi_resource" "hub_routing_appliance" {
type = "Microsoft.Network/virtualNetworkAppliances@2026-05-01"
name = "hub-routing-appliance"
location = azurerm_resource_group.rg_hub.location
parent_id = azurerm_resource_group.rg_hub.id
schema_validation_enabled = false
body = {
properties = {
bandwidthInGbps = 10
privateIPAddressVersion = "IPv4"
subnet = {
id = azurerm_subnet.snet_routing_appliance.id
}
}
}
response_export_values = ["*"]
}
▪ Subnet: must be named VirtualNetworkApplianceSubnet (172.16.0.0/24).
▪ Bandwidth: bandwidthInGbps = 10 sets the appliance capacity.
▪ Schema validation off: the API version is newer than the azapi embedded schemas.
▪ Output: the appliance private IP is exported and used as UDR next hop.

## Slide 8
Steering traffic with User Defined Routes
Each spoke workload subnet gets a route table pointing to the appliance
Azure Network Course | Lab 240 - Virtual Network Routing Appliance
8
resource "azurerm_route" "route-to-nva-spoke1" {
route_table_name = "route-table-to-nva-spoke1"
address_prefix = "10.0.0.0/8"
next_hop_type = "VirtualAppliance"
next_hop_in_ip_address = azapi_resource.hub_routing_appliance
.output.properties.ipConfigurations.0
.properties.privateIPAddress
}
# route table associated to snet-spoke1-workload
# same pattern for spoke2 (route-table-to-nva-spoke2)
Route table | Prefix | Next hop
route-table-to-nva-spoke1 | 10.0.0.0/8 | Appliance IP
route-table-to-nva-spoke2 | 10.0.0.0/8 | Appliance IP
▪ 10.0.0.0/8 covers both spokes (10.1.0.0/16 and 10.2.0.0/16), so spoke-to-spoke traffic goes to the appliance.
▪ Spokes are not peered to each other: the hub peering plus this UDR is the only path between them.
▪ BGP propagation disabled on the route tables (bgp_route_propagation_enabled = false).

## Slide 9
Hub-spoke VNet peering
Azure Network Course | Lab 240 - Virtual Network Routing Appliance
9
resource "azurerm_virtual_network_peering"
"vnet_peering_hub_to_spoke1" {
virtual_network_name = vnet-hub
remote_virtual_network_id = vnet-spoke1
allow_virtual_network_access = true
allow_forwarded_traffic = true
allow_gateway_transit = false
}
# + reverse peering spoke1 -> hub
# + same pair for spoke2
▪ 4 peerings in total: hub<->spoke1 and hub<->spoke2, both directions.
▪ allow_forwarded_traffic = true is required so traffic that the appliance forwards on behalf of another spoke is accepted.
▪ allow_virtual_network_access = true enables basic connectivity between hub and spokes.
▪ No gateway transit in this lab (no VPN / ExpressRoute gateway).

## Slide 10
Traffic flow: spoke1 to spoke2
ping / traceroute from vm-linux-spoke1 to vm-linux-spoke2
Azure Network Course | Lab 240 - Virtual Network Routing Appliance
10
1
vm-linux-spoke1
10.1.0.x sends packet to 10.2.0.x
2
UDR in spoke1
10.0.0.0/8 matches -> next hop = appliance IP
3
Peering to hub
forwarded traffic allowed
4
Routing appliance
routes packet to the spoke2 address space
5
Peering to spoke2
packet delivered to vm-linux-spoke2
Expected traceroute: the appliance private IP (172.16.0.x) appears as an intermediate hop between the two spokes.
The return path follows the same logic through the UDR in spoke2.

## Slide 11
Deploy and verify
Azure Network Course | Lab 240 - Virtual Network Routing Appliance
11
# Deploy
cd 240_vnet_routing_appliance
terraform init
terraform plan -out tfplan
terraform apply tfplan
# Outputs
routing_appliance_ip = "172.16.0.x"
vm_spoke1_ip = "10.1.0.x"
# Connect with Bastion (azureuser) to
# vm-linux-spoke1, then:
ping <vm_spoke2_ip>
traceroute <vm_spoke2_ip>
# Check effective routes
az network nic show-effective-route-table \
-g rg-spoke1-240 -n nic-vm-spoke1 -o table
▪ Effective routes on the spoke NIC should show 10.0.0.0/8 with next hop type VirtualAppliance.
▪ The VMs install traceroute at boot through custom_data (scripts/install-traceroute.sh).
▪ Spot VMs and an ephemeral NVMe OS disk keep the lab cost low.

## Slide 12
Troubleshooting checklist
Azure Network Course | Lab 240 - Virtual Network Routing Appliance
12
▪ Check network interface configuration and IP addresses of the appliance and VMs.
▪ Review route tables / effective routes: is the UDR associated to the workload subnet?
▪ Confirm the peerings are Connected and allow_forwarded_traffic is enabled on both sides.
▪ Inspect appliance logs / diagnostics for errors or misconfiguration.
▪ Test connectivity with ping and traceroute.
▪ Make sure NSGs or firewalls are not blocking the traffic.
▪ Remember: the routing appliance does not filter traffic - security is enforced by NSGs and admin rules.

## Slide 13
Key takeaways
Azure Network Course | Lab 240 - Virtual Network Routing Appliance
13
Route, don't inspect
The routing appliance focuses on scalable east-west routing; pair it with NSGs for security.
UDR is the glue
Route tables with next hop VirtualAppliance send spoke traffic to the appliance IP.
Infrastructure as code
azurerm for network plumbing, azapi for the newer virtualNetworkAppliances resource.
Cleanup: terraform destroy